## Slide 1: Dynamic Multi-core Interference Mitigation
Dynamic Mitigation of Multi-Core Interference in Safety-Critical Systems

## Slide 2: Agenda
Multi-Core Architecture & Interference
Mitigation Strategies
Dynamic Mitigation using WebAssembly
Concept Demonstrator
Evaluation

## Slide 3: Multi-Core ArchitectureS

## Slide 4: Multi-Core Architectures
State of the Art since early 2000 in Workstations, Servers, Embedded, …
Avionics still using Single-Core or Single-Active Core in the 2020s
Why?
Notes: -There is a large gap in the success of multi-core processors between general-purpose systems and avionivs. Why?

## Slide 5: Multi-Core Interference
More: Compute Power
Less: Power, Size, Weight
Enabled by Caches, Interconnects
  → Shared Resources
Advantage
Shared Resources need Arbitration / Allocation policies
→ Temporal Interference between Cores
Problem
AMD/Xilinx Zynq UltraScale+ MPSoC Embedded Design Methodology Guide (UG1228)
Notes: Multi-Core processors are awesome, we want to use them. But the enabler of theses advantages is at the same time the troublemaker in critical-systems

## Slide 6: Multi-Core Interference
Notes: Just a few examples of interference channels in COTS hardware.

## Slide 7: Mitigation Strategies

## Slide 8: Mitigation Strategies
Cache Partitioning
Schedulability Analysis
Disabling Secondary Cores (Single-Active Core)
→ Causes a lot of performance degradation
→ Often only mitigates a specific Interference Channel
→ Requires intricate knowledge of Hardware Implementation
Static Mitigation
Notes: Can we do something about it? Yes, static mitigation techniques exist. But they impede directly on the multi-core advantages and are difficult to apply in general.

## Slide 9: Mitigation Strategies
Trade-Off has to be made
Single-Core
Multi-Core
Temporal Determinism
Multi-Core Interference
Multi-Core Advantages
It’s Not
Multi-Core
Notes: Trade-Off between Single Core Temporal Determinsim and Multi-Core Advantages. What if we could do the trade-off at runtime?

## Slide 10: Mitigation Strategies
Interference degrades Execution Speed
Execution Speed is observable
Interference is caused by Software Execution
Software Execution is controllable
Naïve Idea
Notes: Introduce ingredients of dynamic mitigation

## Slide 11: Mitigation Strategies
Measure Computational Progress
Extrapolate throughput to exp. Time-of-Completion
Control-Loop to keep deadline
Activate Mitigation if necessary
Dynamic Mitigation
Notes: Lets bake a control law.

## Slide 12: Mitigation Strategies
Independent of interference channel mechanism
Catches all interference caused by software
No hardware knowledge required
Advantages
Only one Critical Task can run at any time
All other Tasks have to be considered Non-Critical
Disadvantages
Notes: Advantages of dynamic mitigation in contrast to static techniques.

## Slide 13: Mitigation Strategies
How to measure the Computational Progress?
In Software: Checkpoints
  In known Intervals (fixed amount of Compute between Checkpoints)
  → Intrusive to the Application
In Hardware: Performance Monitoring Unit
  I.e. via Instruction Counting
  → Causes tight coupling between Software and Hardware
Dynamic Mitigation
Notes: How can we actually observe the progress? Checkpoints and PMU is already known, but has drawbacks that must be taken into account, but in virtual hardware (interpreter) it becomes easy.

## Slide 14: Dynamic mitigation with WebAssembly

## Slide 15: WebAssembly
Virtual Instruction Set Architecture
  Not Programming Language
Open, Formal Specification
Strict Spatial Isolation
Strict Type-Checking and Validation at Runtime
→ Potentially valuable for Avionics?
Notes: Short overview over what makes wasm suitable for safety critical

## Slide 16: WebAssembly
Fuel Mechanism
Notes: How does fuel work?

## Slide 17: Dynamic Mitigation with WebAssembly
Wasm Fuel Consumption equals Computational Progress
df := const. Amount of Fuel
throughput = df/dt
Notes: How does fuel-based observation behave in the context of interference.

## Slide 18: Concept Demonstrator

## Slide 19: Concept Demonstrator
Linux based
DLR Wasm Interpreter with a Resumable Fuel Mechanism
StressNG for heavy interference
→ Goal: Show Qualitative Feasibility
Notes: Goal: Show that the idea works in principle, accepting that this specific implementation is not production grade

## Slide 20: Evaluation

## Slide 21: Evaluation
Can WebAssembly Fuel be used to detect Multi-Core Interference?
Is the Dynamic Mitigation Strategy effective?
How efficient is the Dynamic Mitigation?
Notes: First quantitative evaluation of the approach.
What are the questions we want to answer.

## Slide 22: Evaluation
Empirical Evaluation of Computational Throughput
→ WebAssembly Fuel can be used to detect Interference
Detect Interference
Description | Without Interference | With Interference
Mean Throughput | 19.8 ns / fuel | 29.3 ns / fuel
Median Throughput | 9.8 ns / fuel | 9.9 ns / fuel
Median Throughput, only Outliers | 310 ns / fuel | 610 ns / fuel
Notes: Yes, we can use WASM Fuel to observe progress and interference at runtime.

## Slide 23: Evaluation
Statistical Evaluation of N = 100 Runs
→ Dynamic Mitigation is effective
Efficacy 1 / 2
Notes: The control-loop is effective.

## Slide 24: Evaluation
Example: Single Run
Efficacy 2 / 2
Notes: Just an specific example to show the control loop is working.

## Slide 25: Evaluation
Mitigation Activity
→ Less than 10% of Compute on secondary Core remaining
Efficiency
Notes: But it is not efficient. Only a small fraction of multi-core advantages are preserved.

## Slide 26: Limitations & Outlook

## Slide 27: Limitations
Significant Performance Impact due to Interpretation
Only a single Task at any time can be considered “Critical”
Interference originating from the Hardware (DMA, etc) can not be mitigated
General
Assumption of 1 Wasm Instr. ~ 1 Fuel Unit not accurate
Current Primary and Secondary Test Tasks not realistic
Linux based Demonstrator not a suitable Testbed to answer Questions quantitatively
Demonstrator Specific
Notes: limitations

## Slide 28: Outlook
Dynamic Mitigation is promising, but much more Research is necessary
Future Work:
  Port Demonstrator to Bare-Metal setup with proper Tracing
  Switch Test Tasks for more realistic, or more nuanced Tasks
Next Research Requestion:
→ Does this Dynamic Mitigation Approach entail any Temporal Guarantees?
Notes: What next?

## Slide 29: Imprint
Topic: Dynamic Mitigation of Multi-Core Interference in Safety-Critical Systems Date: 2026-02-19
Author: Moritz Meier
Wanja Zaeske
Umut Durak
Institute: Flight Systems (Braunschweig)
Image sources: All images “DLR (CC BY-NC-ND 3.0)” unless otherwise stated